## Slide 1
B. THOMAS GOLISANO COLLEGE OF COMPUTING & INFORMATION SCIENCES
CAPRM-Flood: A Reproducible C++/Python Framework for Property-Level Flood Exposure Indexing
Validated evidence extraction, and the cost of making exact spatial queries cheap
Sterling Alexander sa5836@rit.edu Advisor: Prof. Minseok Kwon M.S. Computer Science | Rochester Institute of Technology | Summer 2026
INTRODUCTION
Flooding is the most common weather-related natural disaster in the United States, and FEMA estimates one inch of water can cause roughly $25,000 of damage to a home. Screening a property for exposure means joining its location to several public hazard datasets, each with a different geometry type, schema, and coordinate reference system.
CAPRM-Flood derives traceable evidence for all 267,362 properties in Monroe County, NY, and validates every spatial computation against an independent implementation. One kernel dominates that work: exact nearest-feature distance, over roughly 1.07 million line segments and polygon boundaries, once per property. Making it cheap without giving up exactness is where the project’s computer-science contribution is concentrated.
PROBLEM & RESEARCH QUESTION
Answered. Can a transparent C++/Python system derive defensible property-level flood evidence reproducibly, validate it across independent implementations, and convert it into an interpretable relative ranking?
Open. The exact geometry is expensive. Learned spatial indexes are evaluated almost exclusively on point data, and several return approximate results. Does the approach extend to exact nearest-neighbour queries over extended objects — line segments and polygon boundaries — and what does exactness cost?
DATA, EVIDENCE FAMILIES & CRS
Evidence family | Public source | Topology | Key derived fields
FEMA flood zone | FEMA National Flood Hazard Layer | Vector polygons | zone, SFHA flag, FLD_AR_ID, match status
Nearest water | USGS 3D Hydrography Program (20 km buffer) | Lines + areas | distance (m), feature id / class / type, tie count
Terrain | USGS 3DEP 1/3 arc-second DEM | Raster grid | elevation, local mean, relative elevation, slope
Precipitation | NOAA precipitation-frequency statistics | Interpolated points | not yet implemented — planned fourth topology
Workload: 267,362 unique NYS parcel-centroid property identifiers, countywide. An immutable 1,000-property fixture is preserved for regression comparison.
All metric work is performed in EPSG:26918 (NAD83 / UTM zone 18N). Distances are never computed in degrees; CRS is recorded as a field on every evidence row.
VALIDATION CONTRACT
Every spatial field is computed twice — once by a Python reference (GeoPandas / Shapely) and once by an independent C++ implementation that shares no code with it. The harness requires full row coverage and field-for-field agreement on polygon match, zone label, SFHA flag, nearest-feature identity, class, name, tie count and CRS, with distance agreement within 1e-6 m. Ties resolve deterministically by lexicographic feature id. Manifests record checksums, row counts, schemas and CRS for every artifact.
SYSTEM ARCHITECTURE
FEMA NFHL
flood-hazard polygons
USGS 3DHP
hydrography lines + areas
USGS 3DEP
elevation raster
Python ingestion · CRS normalization to EPSG:26918 · caching · manifests + checksums
FEMA evidence
table
Nearest-water
evidence table
Terrain evidence
table
Independent C++ kernels — FEMA point-in-polygon · brute force · Feature BVH · Segment BVH
↓
comparison harness: field-for-field agreement, 267,362 / 267,362
Exposure index — four explicitly weighted 0–100 components
Per-property evidence, component scores, index value, countywide percentile rank
Source-family evidence products remain separately inspectable. Scoring is strictly downstream and never mutates evidence.
RESULTS — CORRECTNESS
FEMA membership, Python vs C++ | 267,362 / 267,362
Nearest water, brute force | 267,362 / 267,362
Nearest water, Feature BVH | 267,362 / 267,362
Nearest water, Segment BVH | 267,362 / 267,362
Maximum absolute distance error | 4.658 × 10⁻¹⁰ m
Polygon-interior properties at exactly 0 m | 266, all waterbody
Python test suite | 186 passed
C++ unit suite | 80,021 checks, 0 failures
Automated product audit | 49 pass / 1 warn / 0 fail
The audit checks the stored artifact, not the code. Every unit test passed and the stored percentile still could not be recomputed from the stored index — off by 1.07 × 10⁻² percentile points. The composite lies on a lattice of spacing 9.4 × 10⁻⁶, so float noise near 10⁻¹⁴ was splitting mathematically tied properties into an arbitrary order. Fix: round to 9 decimals before ranking.
RESULTS — EXPOSURE INDEX & RANK STABILITY
Four components, one declared weight each, no hidden sub-weights: FEMA 0.40, nearest water 0.35, absolute elevation 0.15, relative elevation 0.10.
Nearest water
0.653
FEMA zone
0.168
Elevation (abs.)
0.135
Elevation (rel.)
0.043
■ declared weight ■ measured share of index variance
Declared weight is not influence. Water carries 35% of the weight and 65% of the variance; FEMA carries 40% and 17%, because 98.1% of properties are Zone X and a constant cannot change rank — FEMA's role is to move the 1.9% it has information about, decisively.
RANK STABILITY ACROSS 40 REWEIGHTING SCENARIOS
0.0
0.2
0.4
0.6
0.8
1.0
Spearman ρ
min 0.875
median 0.996
Top-decile overlap
min 0.761
median 0.946
grey span = the 4 calibration corners (0.167–0.893): the metric discriminates rather than reporting high correlation by construction
Dashed lines are the stability thresholds, declared in source before any result was measured. Verdict: moderately sensitive — driven by the single worst plausible scenario (equal weighting), not the average.
WHY INDEX GEOMETRY, NOT FEATURES
A bounding-volume hierarchy over whole water features stalls at 93.34% pruning. Arithmetic on its own counters shows why: it examines only 5.498 candidate features per property, yet still performs 70,771 exact segment checks — because it indexes features, not geometry.
The Feature BVH selects features roughly 104× larger than the average water feature.
Lake Ontario, the Genesee River and the Erie Canal are each one enormous feature near almost everything in the county. The bounding box of Lake Ontario is a poor proxy for the distance to Lake Ontario.
DISTANCE-EXACT SEGMENT SPLITTING
Ordering extended objects by a representative point requires inflating the search radius by L/2. Measured L = 5,748.24 m, so inflation would be 2,874 m. Capping sub-segment length at 100 m costs +0.50% index entries, cuts maximum extent 57×, and changes no distance: pieces are collinear with their parent and used only as leaf boxes.
INDEX PROGRESSION
# | Implementation | Indexes | Status
1 | Brute force (no index) | — | implemented, validated
2 | Feature BVH | 2D, 8,572 features | implemented, validated
3 | Segment BVH | 2D, ~1.07M segments | implemented, validated countywide
4 | Hilbert + binary search (control) | 1D, ~1.07M segments | in development
5 | Hilbert + recursive model index | 1D, learned position | in development
6 | Learned search radius | seeds the query disk | planned
Comparisons are adjacent, never global: 3 vs 2 isolates granularity, 4 vs 3 isolates dimensionality reduction, 5 vs 4 isolates the learning itself. Implementation 4 is not optional — without it a loss could not be attributed to either cause.
RESULTS — EXACT-QUERY WORK PRUNED
Brute force
1,063,159
Feature BVH — indexes features
70,771
Segment BVH — indexes geometry
9,717
exact point-to-segment checks per property (log scale)
Indexing segments rather than features prunes 99.09% of exact work — 7.28× fewer checks than the Feature BVH, 109.4× fewer than brute force — while candidate features per property fall from 5.498 to 1.497. Output is byte-identical to the reference, not merely within tolerance.
HEAD-TO-HEAD BENCHMARK
1 Brute force
2 Feature BVH
3 Segment BVH
4 Hilbert + binary search
5 Hilbert + RMI
wall-clock seconds per countywide run, throughput, and traversal counters — pending
Pruning above is measured; wall-clock speedup is not claimed. A single countywide run is not a benchmark — comparison requires repeated runs of all five exact implementations under one protocol, reserved above.
Conclusion. Three evidence families across three data topologies produce one evidence contract for 267,362 properties, with exact Python/C++ agreement at every scale. The open question is whether learned indexing extends to exact nearest-neighbour queries over extended objects — backed by an oracle that can verify exactness rather than assume it.
R·I·T
Rochester Institute of Technology
B. Thomas Golisano College of Computing & Information Sciences
SELECTED REFERENCES
[1] FEMA, National Flood Hazard Layer. [2] USGS 3D Hydrography Program. [3] USGS 3DEP 1/3 arc-second DEM. [4] NYS GIS Program Office, NYS Parcel Centroids.
[5] V. Pandey et al., “How good are modern spatial analytics systems?” PVLDB 11(11), 2018. [6] RLR-Tree, arXiv:2103.04541. [7] “How good are multi-dimensional learned indexes? An experimental survey,” VLDB Journal, 2024.
Repository: github.com/salexander-git/caprm-flood